## Slide 1: Mobile Robots
Taekwon Ga

## Slide 2: Mobile Robotics
Where am I ?
Where am I going ?
How do I get there ?
To answer these questions the robot has to
have a model of the environment (given or autonomously built)
perceive and analyze the environment
find its position/situation within the environment
plan and execute the movement
The Key questions in Autonomous Mobile Robotics
Localization
Path Planning

## Slide 3: Mobile Robotics
Kinematics and motion control

## Slide 4: Mobile Robotics
Wheel Types
Three wheels are sufficient to guarantee the static stability of the vehicle
rolling constraint, no-sliding constraint (lateral)
What wheels to use? How many wheels to use?
Kinematics and motion control

## Slide 5: Mobile Robotics
Kinematics and motion control
Possible Configurations

## Slide 6: Mobile Robotics
Kinematics and motion control
Configuration Space
It has dimensions equal to the number of parameters needed to uniquely describe the configuration of a mobile robot.
Equivalent to the Joint Space for manipulators.

## Slide 7: Mobile Robotics
Kinematics and motion control
Kinematic model of a WMR(wheeled mobile robot)
It represents the allowable directions of motion in the configuration space (allowable velocities)
It is required to deal with common problems of mobile robotics (Navigation, Localization, etc.)

## Slide 8: Mobile Robotics
Kinematics and motion control
Kinematic model of the unicycle model
* Unicycle model : A motorcycle is a vehicle with a single adjustable wheel
The configuration is described by
v is the linear velocity of the contact point, is the angular velocity of the robot
Differential drive is the most popular unicycle type.

## Slide 9: Mobile Robotics
Kinematics and motion control
Kinematic model of the bicycle model
* Bicycle model : A bicycle is a vehicle having a adjustable wheel and a fixed wheel with their rotation axes perpendicular to the longitudinal plane.
The configuration is described by
The model vary depending on the reference point
In practice kinematically equivalent structures but more stable from a mechanical point of view are used.(e.g. Car-like model, Tricycle model)

## Slide 10: Mobile Robotics
Perception

## Slide 11: Mobile Robotics
Sensors for Perception
Tactile sensors or bumpers
  Detection of physical contact, security switches
GPS
  Global localization and navigation
Inertial Measurement Unit (IMU)
  Orientation and acceleration of the robot
Wheel encoders
  Local motion estimation (odometry)
Laser scanners
  Obstacle avoidance, motion estimation, scene interpretation (road detection, pedestrians)
Cameras
  Texture information, motion estimation, scene interpretation

## Slide 12: Mobile Robotics
Localization

## Slide 13: Mobile Robotics
Localization
Map-based localization
  The robot estimates its position using perceived information and a map
  The map
    might be known (localization)
    might be built in parallel (simultaneous localization and mapping – SLAM)
Challenges
  Measurements and the map are inherently error prone
  Thus, the robot has to deal with uncertain information
      → Probabilistic map-based localization
Approach
  The robot estimates the belief state about its position through an SEE and ACT cycle
scan matching process of SLAM

## Slide 14: Mobile Robotics
Localization : the estimation cycle (ACT-SEE)

## Slide 15: Mobile Robotics
Localization : the estimation cycle (ACT-SEE)
SEE: The robot queries its sensors
  → finds itself next to a pillar
ACT: Robot moves one meter forward
  motion estimated by wheel encoders
  accumulation of uncertainty
SEE: The robot queries its sensors again
  → finds itself next to a pillar
Belief update (information fusion)

## Slide 16: Mobile Robotics
Bayes Filter
ACT(motion model) : probabilistic estimation of the robot’s new belief state based on the previous location and the probabilistic motion model with action (control input).
* Theorem of total probability

## Slide 17: Mobile Robotics
Bayes Filter
SEE(observation model) : probabilistic estimation of the robot’s new belief state as a function of its measurement data and its former belief state .
* The Bayes rule

## Slide 18: Mobile Robotics
Bayes Filter
Probability theory is widely and very successfully used for mobile robot localization.
There are many methods for probability-based localization that apply Bayes filters.
  Kalman Filter (KF, EKF, UKF)
  Particle Filter (MCL, AMCL)
  Histogram Filter
  FastSLAM
Further reading:
  “Probabilistic Robotics,” Thrun, Fox, Burgard, MIT Press, 2005.
  “Introduction to Autonomous Mobile Robots”, Siegwart, Nourbakhsh, Scaramuzza, MIT Press 2011
Exercise 1:
  Describe 3 Bayes filter-based localization methods with their features, advantages, and disadvantages

## Slide 19: Mobile Robotics
Particle Filter
The Kalman and Particle filters are algorithms that recursively update an estimate of the state and find the innovations driving a stochastic process given a sequence of observations. The Kalman filter accomplishes this goal by linear projections, while the Particle filter does so by a sequential Monte Carlo method.
The Kalman filter relies on the linearity and normality assumptions. However, many models are non-linear and/or non-gaussian.
Unlike Kalman filter, particle filter can handle non-linear dynamics and non-Gaussian noise distributions

## Slide 20: Mobile Robotics
Particle Filter
1. Prediction Step
For each particle, predict the next state using the system model.

## Slide 21: Mobile Robotics
Particle Filter
2. Correction Step
For each particle, calculate the weight based on the likelihood of the observed measurement given the predicted state
Resample M particles according to their weights. (SIR, Sequantial Importance Sampling)

## Slide 22: Mobile Robotics
Python Example : Particle Filter
Particle Filter example with 4 RFID sensors, the robot can measure a distances from 4 RFID sensors.
true trajectory
dead reckoning trajectory
estimated trajectory with PF

## Slide 23: Mobile Robotics
Python Example : Particle Filter

## Slide 24: Mobile Robotics
Python Example : Particle Filter

## Slide 25: Mobile Robotics
Python Example : Particle Filter
Exercise 2:
  Implement a Particle Filter assuming that data is received from GPS sensors instead of RFID sensors.
  The GPS can measure the robot's 𝑥 and 𝑦 coordinates.
  Covariance matrix of the GPS .
  Assume that the sensor model follows a Multivariate Gaussian Distribution.

## Slide 26: Mobile Robotics
Path Planning

## Slide 27: Mobile Robotics
Path Planning Hierarchy for Mobile Robots

## Slide 28: Mobile Robotics
Path Planning Hierarchy for Mobile Robots
Global Path Planning
To set the overall path from the start to the goal
global view
low frequency
static environment
Local Path Planning
To help the robot follow the global path while avoiding obstacles and optimizing its movement in real-time
local view
high frequency
dynamic environment

## Slide 29: Mobile Robotics
Global Path Planning : Grid-based Planning
Finding the shortest path can be treated as a graph search problem
Suffer from poor scaling in higher dimensions
Algorithms
  Dijkstra’s algorithm
  A* Algorithm
  Breadth-first search
  Depth-first search
A* is very commonly used in robot planning, especially for low-dimensional state spaces.

## Slide 30: Mobile Robotics
Global Path Planning : Sampling-based Planning
Finding a path by randomly sampling the robot's configuration space
efficient in finding paths in high-dimensional spaces, making them suitable for robots with many degrees of freedom
Algorithms
  RRT
  RRT*
  PRM

## Slide 31: Mobile Robotics
Local Path Planning : Dynamic Window Approach
Generating full time-varying trajectories for 𝑉(𝑡) and 𝜔(𝑡) is still very challenging
If we assume (𝑉, 𝜔) are constant for a fixed Δ𝑡, each local path in the future is a circular arc segment
This can be easily considered as a type of velocity configuration space
Maximise utility metric (usually maximise speed, minimize distance to goal, maximise distance from obstacles) across configuration samples
e.g.

## Slide 32: Mobile Robotics
Python Example : Dynamic Window Approach
This is a simple 2D navigation code with Dynamic Window Approach.(No global path planning!)
red cross is a position of the robot and blue cross is a position of the goal.
green line is a predicted trajectory calculated by dynamic window approach controller

## Slide 33: Mobile Robotics
Python Example : Dynamic Window Approach
Algorithm:
1. Sample feasible inputs
2. For each feasible input:
  Simulate trajectory over horizon
  Score trajectory
3. Pick control input that leads to best score
Exercise 3:
  Why don’t we use only a local path planner? Explain why global planning needs to be incorporated.